WEATHER STATION MONITORING USING IOT

Introduction
Weather Monitoring Systems are used to keep track of the ever-changing weather conditions. The
information obtained by such sensors is used to report weather and maintain track of environmental
changes in a given location. Such information is particularly useful in the study of the earth as well as
the analysis of changing climatic and environmental conditions in a given location. Furthermore, the
collected data and analytics can be used in a range of applications, including agriculture, geology,
mining, and building weather forecasting models. A simple weather monitoring system is built in this
project, which can monitor the temperature, humidity, barometric pressure and rain condition of a
location.
## What is the ESP8266 WiFi Module?
The ESP8266 is a low-cost Wi-Fi microcontroller chip developed by Espressif Systems, based in Shanghai, China. It quickly became a game-changer for DIY enthusiasts, IoT developers, and students because it made wireless connectivity both affordable and easily accessible.Wifi modules or wifi microcontrollers are used to send and recieve data over Wi-Fi. They can also accept commands over the Wi-Fi. Wi-Fi modules are used for communications bewtween devices. They are most commonly used in the field of Internet of Thnigs.

Key Features:
Wi-Fi Connectivity: Supports IEEE 802.11 b/g/n standards, operating in the 2.4 GHz band.
Processor: 32-bit RISC processor based on Tensilica Xtensa L106.
Memory: Includes 32KB instruction RAM, 32KB instruction cache RAM, 80KB user data RAM, and external QSPI flash memory (up to 16MB).
Interfaces: Provides a variety of communication interfaces including SPI, I2C, UART, and I2S.
Operating Modes: Can function as a Station (connecting to an existing Wi-Fi network) or a Soft Access Point (creating its own Wi-Fi network).
Security: Supports various security protocols like WEP, WPA, and WPA2.
GPIO Pins: Features multiple GPIO pins for controlling digital I/O, which can be configured for various functions like I2C, I2S, UART, PWM, etc.
ADC: Includes a 10-bit ADC for reading analog inputs.
Power Consumption: Designed for low power consumption, making it suitable for battery-operated devices.
Programming: Can be programmed using languages like Arduino, MicroPython, and Lua.
Applications: Commonly used in IoT applications, including smart home automation, remote devices, and data logging.